## Slide 1: Statistical methods of global air pollution modeling
University of Utrecht, The Netherlands
Meng Lu

## Slide 2: S1 Air pollution mapping and data exploration Introduction Land use regression model Data Scripts data exploration: from visualization to preliminary examination S2 Machine learning methods Introduction machine learning methods Scripts How to use them, modeling parameter tuning, partial dependence plot, variable importance S3 Prediction (map) and result analysis Scripts Predicting using Lasso, random forest, xgboost Results

## Slide 4: Land use regression and data used in the project
Part 1

## Slide 5: Predicting air pollution and analyzing the sources.
Sensor measurements:
Station measurements
Mobil sensors
GIS predictors:
Population
Road length within a buffer
Distance to roads
Traffic load
…
Remote sensing measurements:
OMI (250 km)
Tropomi (8 km)
…
Land use regression (LUR)

## Slide 6
25 m buffer
1000 m buffer
Buffered predictors
Notes: x

## Slide 7: LUR prediction of NO2
Hour
0
5km
0
60
30
5 m resolution
Spatiotemporal dynamic of air pollution showing road effects

## Slide 8
Ground monitor Data: OpenAQ
(2017)

## Slide 9
Road types: Highway, primary roads, local roads
Emission-related
Road length and industry area within 25 m – 300 m radius ring
Background
Road length within 300 m - 5000 m radius ring
Population: 1 km, 3 km, 5 km
Industry area 300m - 5km
Monthly wind speed (0.5 degree)
Monthly temperature (0.5 degree)
Surface concentration product from Satellite products and the GEOS-CHEM
Satellite measured NO2 column density
Predictors

## Slide 10
Tropomi
Feb 2018 to Jan 2019

## Slide 11: Remote sensing measurements: OMI (Ozone Monitoring Instrument)
At nadir 13 km × 24 km
Zoom in mode 13 km× 12 km
Daily global coverage
Spectral bands: ultraviolet and visible (270 to 500 nm)
Date of Launch | 15 July 2004
NO2, SO2, BrO, OCIO, O3 (36 km × 48 km)

## Slide 12: surface product based on remote sensing and GEOS-CHEM
Chemical transportation models: GEOS-CHEM
global prediction are of coarse resolution - > integrating RS data
Surface NO2 product made using GEOS-CHEM together with GOME, SCIAMACHY, and GOME-2 satellite instruments. http://fizz.phys.dal.ca/~atmos/martin/?page_id=232
The surface product is used in our model.

## Slide 13
Road length | https://www.openstreetmap.org/
Industrial area | https://www.openstreetmap.org/
Population | http://www.integrated-assessment.eu/eu/index.html
Elevation | https://www2.jpl.nasa.gov/srtm/
Wind speed | https://confluence.ecmwf.int/pages/viewpage.action?pageId=74764925
Temperature | https://confluence.ecmwf.int/pages/viewpage.action?pageId=74764925
TROPOMI | http://www.tropomi.nl
NO2 Surface product | http://fizz.phys.dal.ca/~atmos/martin/?page_id=232
OMI | https://mirador.gsfc.nasa.gov/cgi-bin/mirador/presentNavigation.pl?tree=project&dataset=OMNO2d.003&project=OMI&dataGroup=L3_V003&version=003&CGISESSID=57642d429543194f1007d9b91bfab0ae

## Slide 14: Statistical learning 1980, computer science, machine learning, neural networks, zipcode recognision problem, bell lab
Part 2 (1)

## Slide 15: Statisitcal learning

## Slide 16
Bias-variance trade-off
All algorithms are affected by bias-variance trade-off

## Slide 17
Regularization
Lasso regression
Ridge regression

## Slide 18
Lasso vs. Ridge
ElasticNet

## Slide 19: Regression trees
Features:
Non-parametric
Different kinds of variables
Redundant variables are ignored
Handle missing data
Small trees are easy to interpret
Dominance
Boosting > Randomforest > bagging > single tree
Is it true that boosting trees are always better than the randomforest?
Leveraging trees to improve the performance:
Bagging
Boosting
Random forest

## Slide 20: Random forest
variance reduction
(tunning parameter: number of trees, tree depth)
Identically distributed variables, each has variance 2
An average of B of i.i.d random variables has variance
If the variables are not independent (but identically distributed) with positive pairwise correlation , the variance of the average:
“the more uncorrelated, the more you bringing down the variance”.

## Slide 21
Limitation:
Bias towarding variables with many splits or missing variables, does not assess uncertainty
Variations:
Recursive partition trees:
Hypothesis testing of dependency between variables and resursively fitting the splitting weight
Baysian based sampling and variable selection:
Baysian framework for 1 and 2
Quantile random forest:
Estimate quantiles (beyond the conditional mean)
For each tree:
Bootstraping sample D* from the training data D
Draw m* variables randomly from all variables m, pick the best split-point (variable), split the node.
More details

## Slide 22
Stochastic gradient Boosting (regression)
-- Reweight based on the previous trees, stage-wise fitting
Each successive tree is built for the prediction residuals of the preceding tree in an adaptive way to reduce bias.
.
initial:
r = y
fit a regression tree to r: g(x)
for each tree:
f(x) = e*g(x)
r = r – f(x)
(r: residual; e: learning rate)
(Stochastic) Gradient Boosting
approach the gradient of the loss function (e.g. binomial, logistic, poison) by trees.
Each consecutive tree is built for the prediction residuals (from all preceding trees) of an independently drawn random sample

## Slide 23
Stochastic Gradient Boosting
Each consecutive tree is built for the prediction residuals (from all preceding trees) of an independently drawn random sample
Learning Rate

## Slide 24
XGboost
Exteme gradient boosting
Features
Parallel computation
Support dense and sparse matrix
Can costomize objective fucntions
obj(θ) = L(θ) + Ω(θ)
Idea
Not only impurity, but also model complexity

## Slide 25
nrounds:
Controls the maximum number of iterations.
Tuned by CV
Eta:
Controls the learning rate,
It must be supported by increase in nrounds.
max_depth:
It controls the depth of the tree. Larger data sets require deep trees to learn the rules from data.
Tuned by CV
Gamma:
      Controls regularization (or prevents overfitting).
      Higher the value, higher the regularization. Regularization means penalizing large coefficients which don't improve the model's performance.
      If you see train error >> test error, bring gamma into action.
Norms:
L1 norm (alpha) and L2 norm (lambda)
Hyperparameters

## Slide 26
Lasso regularization of regression trees
--- discarding trees that are not useful
Postprocessing

## Slide 27: What can the machine learning methods tell? Partial dependence plot, trees, variable importance
Part 2 (2)

## Slide 28
Visualizing a tree
ROAD_M345: secondry
and local roads
Pop_: population
ROAD_2: primary roads
ROAD_1: highway
A closer look at the model

## Slide 29
Partial dependence.
-- Shows the relationship between the target and a feature.
Assumption: the features in C are not correlated with the features in S
Xs : the features of the partial dependence function
Xc: the other features used in the machine learning model
Marginalizing the model output over the distribution of the features in set C,

## Slide 31
30m
120000m
5000m
ROAD 2, 50m
Population, 3km
ROAD M345, 300m
ROAD M345, 300m
Population, 3km
ROAD 2, 50m
Correlation:
0.3
Correlation:
0.4
Correlation:
0.16

## Slide 32
Partial dependent plots: Linear regression
Population, 3km
ROAD M345, 300m
ROAD 2, 50m
ROAD M345, 300m
Population, 3km

## Slide 33
Partial dependent plots: Random forest
30m
120000m
5000m
Population, 3km
ROAD M345, 300m
ROAD 2, 50m
Population, 3km
ROAD M345, 300m
Population, 3km
ROAD M345, 300m
40
4000

## Slide 34
Partial dependent plots: stochastic gradient boosting
30m
120000m
5000m
Population, 3km
ROAD M345, 300m
ROAD 2, 50m
Population, 3km
ROAD M345, 300m

## Slide 35: predicting and results
Part 3

## Slide 36
Germany
highway
primary

## Slide 37
Germany
RMSE: root mean squared error
MAE: mean absolute error
IQR: interquartile range
LM: Multiple linear regression
RF: random forest
SGB: Stochastic gradient boosting
XGB: xgboost

## Slide 38
Global model
Ranked top 20 by Random Forest* Primary road 50 m, 100 m Ranked top 20 by XGBoost Primary road 50 m, 100 m Highway 100 m Local road 25 m, 50 m, 100 m Selected by LASSO Primary road 50 m, 100 m Highway 50 m, 100 m Local road 25 m, 50 m, 100 m
National model of Germany
Ranked top 20 by Random Forest Primary road 25m, 50 m, 100 m Local road 25m, 50 m, 100 m, 300 m Ranked top 20 by XGBoost Primary road 50 m, 100 m Highway 50 m Local road 25m, 50 m, 100 m, 300 m Selected by LASSO Primary road 25m, 50 m, 100 m Highway 50m, 100 m Local road 100 m, 300m
Important emition-related variables
*Highway 100 m ranked 26

## Slide 39
US
highway
primary

## Slide 40
primary
Spain
highway

## Slide 41
Random Forest
Prediction: China
highway
primary

## Slide 42
ROAD_M345: secondry and local roads
Pop_: population ROAD_2: primary roads
Global model
Variable importance

## Slide 43
ROAD_M345: secondry and local roads
Pop_: population ROAD_2: primary roads
Variable importance
Germany

## Slide 44
http://rpubs.com/menglu/473973
Using random forest for Geostatistic-like interpolation