## Slide 1: Global air pollution modelling
University of Utrecht, The Netherlands
Global and geo-health data center
Meng Lu

## Slide 2: Overview
Introduction
Spatio-temporal epidemiology
Air pollution modelling and exposure assessment for health research
Global air pollution modelling

## Slide 3
Spatio-temporal Epidemiology
Spatiotemporal epidemiology: The description and analysis of geographical data, specifically health outcome data and factors that may explain variations in these outcome data over space. factors: environmental, demographic, genetic, habits, infectious risk factors.
Environmental epidemiology: Spatiotemporal epidemiology that focuses on how environmental exposures impact human health.
Origin
1854 John Snow,
Identify possible causes of cholera outbreaks.

## Slide 5: Exposome
Link environment to health:
Challenge: detailed space-time paths over a large population and long time period may not be available.
work
Agent-based modelling approach
weekdays | 00:00 - 08:00 08:00 - 09:00 08:10 - 17:00 17:00 - 18:00 17:09 - 23:59 | home commuting work commuting home

## Slide 6: Take a deep breath

## Slide 7: Air pollution -- Consists of chemicals or particles in the atmosphere that poses health and environmental threats.
Mortality:
World: more than 3.2 8.8 millions death a year

## Slide 8: Most measured air pollutants and their health impacts O3 NO2 SO2 CO PMx Little is known about how air pollutant affect health over a population
Source [2]

## Slide 9: Why is global air pollutant mapping and exposure assessment important?
Station measurements
Unequally distributed ground monitors
Consistent comparison
Shaddock et al., 2018

## Slide 10: Remote sensing measurements: OMI (Ozone Monitoring Instrument)
At nadir 13 km × 24 km
Zoom in mode 13 km× 12 km
Daily global coverage
Spectral bands: ultraviolet and visible (270 to 500 nm)
Date of Launch | 15 July 2004
NO2, SO2, BrO, OCIO, O3 (36 km × 48 km)

## Slide 11
Tropomi
(TROPOspheric Monitoring Instrument)
launched 2017, available from Feb 2018
Souce [3]
7 km x 7 km

## Slide 12
Tropomi
Spectral bands:
ultraviolet and visible (270–500 nm), near-infrared (675–775 nm), shortwave infrared (2305–2385 nm) spectral bands.
zoom in mode: 7 km × 3.5 km
NO2, O3 (7km × 28km), SO2, methane and CO

## Slide 13
Spectral bands of Tropomi

## Slide 14: Air pollution modelling methods
Statistical methods: regression, Kriging
Chemical transportation models: GEOS-CHEM
Hybrid: Kalman filter

## Slide 15: Predicting air pollution and analyzing the sources.
Sensor measurements:
Station measurements
Mobil sensors
GIS predictors:
Population
Road length within a buffer
Distance to roads
Traffic load
…
Remote sensing measurements:
OMI (250 km)
Tropomi (8 km)
…
Land use regression (LUR)

## Slide 16: Predictor variables in buffers
25m buffer
1000m buffer
Major road length
Notes: x

## Slide 17: LUR Prediction
Hour
0
5km
0
60
30
5 m resolution
Spatiotemporal dynamic of air pollution showing road effects

## Slide 18
Global NO2 mapping: Larken et al. 2017 (100m):
LUR model
Lasso, continental variable as prediction
Limitations:
Linear relationship
Road effects not modelled
Only evaluated by Rsquared and RMSE
Does not include RS measurement

## Slide 19
Can tree-based machine learning methods and Tropomi improve global NO2 mapping ?

## Slide 20
Data: OpenAQ

## Slide 21
Emission-related
Road length within 25 m – 300 m radius ring
- Highway, primary roads, secondary roads, tertiary roads, unpaved roads
Industry area within 25 m – 300 m radius ring
Background
Road length within 300 m - 5000 m radius ring
Population: 1 km, 3 km, 5 km
Industry area 300m - 5km
Monthly wind speed (0.5 degree)
Monthly temperature (0.5 degree)
Surface concentration from Satellite products and the GEOS-CHEM
Satellite measured NO2 column density
Distance to coast
Predictors

## Slide 22
Regularized regression
Trees-based
- Random forest
Stochastic gradient boosting
Extreme gradient bossting
Mechamical model
- Nonlinear regression integrating air distribution mechanisms
Ridge
Lasso
ElasticNet
Method
Compare global and national models
Comparing different statistical learning methods
Four national models:
US (100),
China (1400),
Germany (350),
Spain (350)
A global model

## Slide 23
Paired correlation: separating between day and night
germany
Local roads
Primary roads
Tropomi
Data

## Slide 24
Result: global model accuracy
RMSE: root mean squared error
MAE: mean absolute error
IQR: interquartile range
LM: Multiple linear regression
RF: random forest
SGB: Stochastic gradient boosting
XGB: xgboost

## Slide 25
Result: global and national models
RF vs. Lasso
CN: China
DE: Germany
ES: Spain
Conclusion: random forest is more suitable than Lasso for a global NO2 maping and using random forest can achieve an accuracy as good as national models.

## Slide 26
Germany
highway
primary

## Slide 27
Global model
Ranked top 20 by Random Forest* Primary road 50 m, 100 m Ranked top 20 by XGBoost Primary road 50 m, 100 m Highway 100 m Local road 25 m, 50 m, 100 m Selected by LASSO Primary road 50 m, 100 m Highway 50 m, 100 m Local road 25 m, 50 m, 100 m
National model of Germany
Ranked top 20 by Random Forest Primary road 25m, 50 m, 100 m Local road 25m, 50 m, 100 m, 300 m Ranked top 20 by XGBoost Primary road 50 m, 100 m Highway 50 m Local road 25m, 50 m, 100 m, 300 m Selected by LASSO Primary road 25m, 50 m, 100 m Highway 50m, 100 m Local road 100 m, 300m
Important emition-related variables
*Highway 100 m ranked 26

## Slide 28
Germany
RMSE: root mean squared error
MAE: mean absolute error
IQR: interquartile range
LM: Multiple linear regression
RF: random forest
SGB: Stochastic gradient boosting
XGB: xgboost

## Slide 29
emission-related variables
xgb: xgboost
RF: random forest
Prediction from different methods
highway
primary

## Slide 30
China
RMSE: root mean squared error
MAE: mean absolute error
IQR: interquartile range
LM: Multiple linear regression
RF: random forest
SGB: Stochastic gradient boosting
XGB: xgboost

## Slide 31
Conclusion
The validation results indicate that tree-based methods are more suitable than Lasso for a global NO2 maping and their global models can achieve an accuracy as good as national models.
The differences in validataion accuracy between statistical learning methods are small.
The patterns of spatial predictions using different methods are notably different.
Field tracking measurements may be needed for validation.

## Slide 32: Thank you

## Slide 33
[1] Shaddock et al., 2018: Environ. Sci. Technol.201852169069-9078
[2] https://www.theguardian.com/sustainable-business/2016/jul/05/how-air-pollution-affects-your-health-infographic
[3] http://www.tropomi.eu/sites/default/files/files/agu_veefkind.pdf

## Slide 34
US
highway
primary

## Slide 35
primary
Prediction: Spain
highway

## Slide 36
China
RMSE: root mean squared error
MAE: mean absolute error
IQR: interquartile range
LM: Multiple linear regression
RF: random forest
SGB: Stochastic gradient boosting
XGB: xgboost

## Slide 37
Random Forest
Prediction: China
highway
primary