## Slide 1: Statistical methods of global air pollution modeling
University of Utrecht, The Netherlands
Meng Lu

## Slide 2: 1. Introduction to air pollution mapping and data exploration hands-on 1 (10 mins): “getting ready” install packages, visualize data, data exploration: paired correlations, spatial dependence and scatterplot 2. Machine learning methods ensemble trees, mixed-effect models, artificial neural network, convolutional neural networks hands-on 2 + break (45 mins): “machine learning methods.” 3. Modelling process hands-on 3 (15 mins): “modelling process” hyper-parameter optimization, bootstrapping-based cross-validation, mapping and compare spatial patterns of different predictions

## Slide 3: Introduction and data
Part 1

## Slide 4: Predicting air pollution and analyzing the sources.
Sensor measurements:
Station measurements
Mobil sensors
GIS predictors:
Population
Road length within a buffer
Distance to roads
Traffic load
…
Remote sensing measurements:
OMI (250 km)
Tropomi (8 km)
…
Land use regression (LUR)

## Slide 5
25 m buffer
1000 m buffer
Buffered predictors
Notes: x

## Slide 6: LUR prediction of NO2
Hour
0
5km
0
60
30
5 m resolution
Spatiotemporal dynamic of air pollution showing road effects

## Slide 7
Ground monitor Data: OpenAQ
(2017)

## Slide 8
Tropomi
Feb 2018 to Jan 2019

## Slide 9: Remote sensing measurements: OMI (Ozone Monitoring Instrument)
At nadir 13 km × 24 km
Zoom in mode 13 km× 12 km
Daily global coverage
Spectral bands: ultraviolet and visible (270 to 500 nm)
Date of Launch | 15 July 2004
NO2, SO2, BrO, OCIO, O3 (36 km × 48 km)

## Slide 10: Surface product based on remote sensing and GEOS-CHEM
Chemical transportation models: GEOS-CHEM
global prediction are of coarse resolution - > integrating RS data
Surface NO2 product made using GEOS-CHEM together with GOME, SCIAMACHY, and GOME-2 satellite instruments. http://fizz.phys.dal.ca/~atmos/martin/?page_id=232
The surface product is used in our model.

## Slide 11
Geospatial predictors
Road and industrial area from OpenStreetMap (vector)
Earth nightlight (500 m)
as a proxy for socio-demographics
Population (100 m)
From human settlement layers
Wind speed and temperature
Elevation: SRTM (90 m)

## Slide 12
Hands-on 1: Setup and data visualization
In the folder R_scripts
Data_visualize/Openaq.Rmd:
query station measurements from OpenAQ API
Data_visualize/ Plot_RS.Rmd:
visualize TROPOMI and OMI satelite measurements
Introduction/GeoHub2020.Rmd:
run the chunks till “modelling” for data exploration

## Slide 13: Machine learning 1980, computer science, machine learning, neural networks, zipcode recognision problem, bell lab
Part 2

## Slide 14
Bias-variance trade-off
All algorithms are affected by bias-variance trade-off

## Slide 15: Machine learning

## Slide 16
Go deep
Road density
Road structure

## Slide 17
population
> 1000/km2
< 1000/km2
Traffic count
> 500/hr
< 500/hr
22.5 µg/m3
20.0
µg/m3
10.0
µg/m3
Regression trees
Hungry
yes
no
Local food
Yes
No
sausage
Japanese food
Do sports
A decision tree
Features:
Non-parametric
Different kinds of variables
Redundant variables are ignored
Handle missing data
Small trees are easy to interpret

## Slide 18: Ensemble trees -- reducing model variance
Dominance
Boosting > Randomforest > bagging > single tree
Is it true that boosting trees are always better than the randomforest?
Bagging
Random forest
Boosting

## Slide 19: Random forest
variance reduction
(tunning parameter: number of trees, tree depth)
Identically distributed variables, each has variance 2
An average of B of i.i.d random variables has variance
If the variables are not independent (but identically distributed) with positive pairwise correlation , the variance of the average:
“the more uncorrelated, the more you bringing down the variance”.

## Slide 20: Random forest
Hyperparameters:
Number of trees
Number of variables
Minimum observations at leaf
R_scripts/Introduction/shiny_randomforest/app.R

## Slide 21
Limitation:
Bias towarding variables with many splits or missing variables, does not assess uncertainty
Variations:
Recursive partition trees:
Hypothesis testing of dependency between variables and resursively fitting the splitting weight
Baysian based sampling and variable selection:
Baysian framework for 1 and 2
Quantile random forest:
Estimate quantiles (beyond the conditional mean)
For each tree:
Bootstraping sample D* from the training data D
Draw m* variables randomly from all variables m, pick the best split-point (variable), split the node.
More details

## Slide 22
Stochastic gradient Boosting
-- Reweight based on the previous trees, stage-wise fitting
Each successive tree is built for the prediction residuals of the preceding tree in an adaptive way to reduce bias.
.
initial:
r = y
fit a regression tree to r: g(x)
for each tree:
f(x) = e*g(x)
r = r – f(x)
(r: residual; e: learning rate)
(Stochastic) Gradient Boosting
approach the gradient of the loss function (e.g. binomial, logistic, poison) by trees.
Each consecutive tree is built for the prediction residuals (from all preceding trees) of an independently drawn random sample

## Slide 23
Stochastic Gradient Boosting
Each consecutive tree is built for the prediction residuals (from all preceding trees) of an independently drawn random sample
Learning Rate

## Slide 24
XGboost
Exteme gradient boosting
Features
Parallel computation
Support dense and sparse matrix
Can costomize objective fucntions
obj(θ) = L(θ) + Ω(θ)
Idea
Not only impurity, but also model complexity

## Slide 25
Control overfitting: Regularization
Lasso regression
Ridge regression

## Slide 26
nrounds:
Controls the maximum number of iterations.
Eta:
learning rate,
max_depth:
the depth of the tree.
Gamma:
Penalizing large coefficients which don't improve the model's performance.
Alpha L1 norm (Lasso)
Lambda L2 norm (Ridge)
Hyperparameters

## Slide 27
1 tree
100 trees
https://lumeng0312.shinyapps.io/xgboost/?_ga=2.179522658.79817579.1592385947-986486774.1592216474
Please try this QR code if the link does not work.
R_scripts/Introduction/shiny_xgboost/app.r

## Slide 28
Lasso regularization of regression trees
--- discarding trees that are not useful
Postprocessing

## Slide 29: Deep learning: neural networks
g()
Bias b: x1 = 1
A perceptron

## Slide 30: Learning: optimizing the loss
Regression:
Mean Squared Error
Classification:
Cross-entropy

## Slide 31: Deep learning: neural networks

## Slide 32
Convolutional neural networks
R_script/convolution_filter/convolution_illusrated
Convolutional filter

## Slide 33
Regularization
Batch normalization
Drop-out

## Slide 34
ResNet
Making networks deeper

## Slide 35
Hands-on 2: Ensemble tree-based methods
From R_scripts/Introduction/GeoHub2020.Rmd:
run the chunks from “modelling” for different modelling approach.
Kaggle notebook

## Slide 36
Hands-on 3: Modeling process
From R_scripts/modeling process
You can find the three R markdown files corresponding to hyper-parameter tunning, cross-validation and mapping.

## Slide 37: What can the machine learning methods tell? Partial dependence plot, trees, variable importance
Part 2 (2)

## Slide 38
Visualizing a tree
ROAD_M345: secondry
and local roads
Pop_: population
ROAD_2: primary roads
ROAD_1: highway
A closer look at the model

## Slide 39
Partial dependence.
-- Shows the relationship between the target and a feature.
Assumption: the features in C are not correlated with the features in S
Xs : the features of the partial dependence function
Xc: the other features used in the machine learning model
Marginalizing the model output over the distribution of the features in set C,

## Slide 41
30m
120000m
5000m
ROAD 2, 50m
Population, 3km
ROAD M345, 300m
ROAD M345, 300m
Population, 3km
ROAD 2, 50m
Correlation:
0.3
Correlation:
0.4
Correlation:
0.16

## Slide 42
Partial dependent plots: Linear regression
Population, 3km
ROAD M345, 300m
ROAD 2, 50m
ROAD M345, 300m
Population, 3km

## Slide 43
Partial dependent plots: Random forest
30m
120000m
5000m
Population, 3km
ROAD M345, 300m
ROAD 2, 50m
Population, 3km
ROAD M345, 300m
Population, 3km
ROAD M345, 300m
40
4000

## Slide 44
Partial dependent plots: stochastic gradient boosting
30m
120000m
5000m
Population, 3km
ROAD M345, 300m
ROAD 2, 50m
Population, 3km
ROAD M345, 300m

## Slide 45: predicting and results
Part 3

## Slide 46
Germany
highway
primary

## Slide 47
Germany
RMSE: root mean squared error
MAE: mean absolute error
IQR: interquartile range
LM: Multiple linear regression
RF: random forest
SGB: Stochastic gradient boosting
XGB: xgboost

## Slide 48
Global model
Ranked top 20 by Random Forest* Primary road 50 m, 100 m Ranked top 20 by XGBoost Primary road 50 m, 100 m Highway 100 m Local road 25 m, 50 m, 100 m Selected by LASSO Primary road 50 m, 100 m Highway 50 m, 100 m Local road 25 m, 50 m, 100 m
National model of Germany
Ranked top 20 by Random Forest Primary road 25m, 50 m, 100 m Local road 25m, 50 m, 100 m, 300 m Ranked top 20 by XGBoost Primary road 50 m, 100 m Highway 50 m Local road 25m, 50 m, 100 m, 300 m Selected by LASSO Primary road 25m, 50 m, 100 m Highway 50m, 100 m Local road 100 m, 300m
Important emition-related variables
*Highway 100 m ranked 26

## Slide 49
US
highway
primary

## Slide 50
primary
Spain
highway

## Slide 51
Random Forest
Prediction: China
highway
primary

## Slide 52
ROAD_M345: secondry and local roads
Pop_: population ROAD_2: primary roads
Global model
Variable importance

## Slide 53
ROAD_M345: secondry and local roads
Pop_: population ROAD_2: primary roads
Variable importance
Germany

## Slide 54
http://rpubs.com/menglu/473973
Using random forest for Geostatistic-like interpolation

## Slide 55
Road length | https://www.openstreetmap.org/
Industrial area | https://www.openstreetmap.org/
Population | http://www.integrated-assessment.eu/eu/index.html
Elevation | https://www2.jpl.nasa.gov/srtm/
Wind speed | https://confluence.ecmwf.int/pages/viewpage.action?pageId=74764925
Temperature | https://confluence.ecmwf.int/pages/viewpage.action?pageId=74764925
TROPOMI | http://www.tropomi.nl
NO2 Surface product | http://fizz.phys.dal.ca/~atmos/martin/?page_id=232
OMI | https://mirador.gsfc.nasa.gov/cgi-bin/mirador/presentNavigation.pl?tree=project&dataset=OMNO2d.003&project=OMI&dataGroup=L3_V003&version=003&CGISESSID=57642d429543194f1007d9b91bfab0ae

## Slide 56
nrounds:
Controls the maximum number of iterations.
Tuned by CV
Eta:
Controls the learning rate,
It must be supported by increase in nrounds.
max_depth:
It controls the depth of the tree. Larger data sets require deep trees to learn the rules from data.
Tuned by CV
Gamma:
      Controls regularization (or prevents overfitting).
      Higher the value, higher the regularization. Regularization means penalizing large coefficients which don't improve the model's performance.
      If you see train error >> test error, bring gamma into action.
Norms:
L1 norm (alpha) and L2 norm (lambda)
Hyperparameters

## Slide 57
Convolution and deconvolution